## Slide 1: Vivado Design Flow
Artix-7
Vivado 2015.2 Version

## Slide 2: Outline
Vivado IDE Features and Benefits
Vivado Design Suite Introduction
Vivado Design Flow

## Slide 3: Who Should Use Vivado?
Designers needing an interactive design approach
  Analysis and area constraints to drive place & route
Challenging designs
  Large devices, complex constraints, and high device utilization
  Advantages are also seen with small devices
Designs experiencing implementation issues
  Performance, capacity, run time, and repeatability
Designs requiring implementation control
  Users looking for options other than just a pushbutton flow
  Visualize design issues from many aspects
  Block-based design constraints
Notes: Typical designers are involved in complex, high-density designs. They do not mind using a more interactive and iterative approach, as opposed to a pushbutton flow (as long as it produces improved timing results). Vivado IDE users also include those who want to be more involved (in control) of what the implementation tools are doing.
The productivity gains enabled by the Vivado IDE will help reduce the overall implementation iterations required by these types of designs.
Typical designers need extra performance and have experienced implementation issues previously.
Often, complex designs require many iterations to finalize the performance. This is because designers run the risk of not meeting their timing with each iteration when running implementation on the entire design. The use of area constraints can improve the consistency of your timing results, although it does not guarantee meeting your timing objectives.

## Slide 4: Vivado’s Visualization Feature
Visualize and debug your design at any flow stage
  Cross-probing between netlist/schematic/RTL

## Slide 5: Outline
Vivado IDE Features and Benefits
Vivado Design Suite Introduction
Vivado Design Flow

## Slide 6: Getting Started Jump Page
All buttons grouped by functionality
Quick Start
  Previous projects can quickly opened
  Links to create new or example projects
Tasks
  IP management, hardware manager, Tcl Store
Helpful links
  Documentation and Tutorials
    Invokes PDF viewer for documentation
  Quick Take Videos
  Release Notes Guide
Tcl Console for command line access

## Slide 7: New Project Creation Wizard
Very first step is project creation with five choices
Five different types of projects:
  RTL
    Front-to-back (even for Block Designs)
  Post-synthesis
    EDIF or NGC
  I/O planning
    For early pin testing
    No design sources
  Import Project
    Imports existing project from Synplify, XST, or ISE
  Example Project
Notes: RTL Project:
The RTL Project environment enables analysis of the compiled RTL design including logic exploration, resource and power estimation, DRCs, and I/O pin planning.
Post-synthesis Project:
This is where pre-implementation design analysis, debug core insertion, and constraint definition is performed. You can explore various constraints sets, devices, and implementation options.
Import ISE tool results:
The Implemented Design environment loads the netlist and implementation results directly from the run directory to ensure that the viewed data represents the launched run.

## Slide 8: Project creation flow (RTL/Synthesized Design)
Defines the project name and location
Select source files in RTL project creation
  All recognized source files, Verilog, VHDL, in the directory and subdirectories, can be added
Select post-synthesized netlist in Post-synthesized project creation
  All synthesized files in the directory and subdirectories, are added
Select constraint files
  One or more constraints files including IP specific and top-level can be added
Select target device or pre-defined board
Reference original existing files or import and copy them into the project

## Slide 9: Project Data
All project data is stored in a project_name directory containing the following basic set of directories:
  project_name.xpr file: Vivado project file, contains project settings
  project_name.runs directory: Contains all run data
  project_name.srcs directory: Contains all imported local HDL source files, netlists, and XDC files
  project_name.data directory: Stores floorplan and netlist data

## Slide 10: Journal and Log Files
Journal file (vivado.jou)
  Contains just the Tcl commands executed by the Vivado IDE
Log file (vivado.log)
  Contains all messages produced by the Vivado IDE, including Tcl commands and results, info/warning/error messages, etc.
Location
  Linux: directory where the Vivado IDE is invoked
  Windows via icon: %APPDATA%\Xilinx\Vivado or C:\Users\<user_name>\AppData\Roaming\Xilinx\Vivado
  Windows via command line: directory where the Vivado IDE is invoked
  From the GUI
    Select File > Open Log File
    Select File > Open Journal File

## Slide 11: Constraints File Management
Constraint sets are a collection of XDC files
  A project can contain multiple constraint sets
  For a constraints set to be applied, it must be set to "active"
    Any constraint set can be made active by right-clicking and selecting Make Active
Target XDC
  The XDC file in a constraint set to which new constraints are written
    From the Constraints Wizard for example
  Target XDC can be specified by right-clicking and selecting Set As Target Constraint File

## Slide 12: Project Navigator
Used to manage sources, customize IP, and view project details in the Project Summary
Flow Navigator
Sources view
  Hierarchical display of sources, including constraints files
  IP Sources and Libraries view
    HDL and netlists including references to library and location
Project Summary
  Gives access to device utilization (resources), timing summary, and strategy information
Tcl Console, Messages, Compilation, Reports, and Design Runs

## Slide 13: Project Settings
General settings
  Select device
  Target HDL language
  Simulation tool (Vivado simulator included)
  Top module name
  Language options
Other settings are covered in their respective modules

## Slide 14: Flow Navigator – RTL Project
Configure project sources
  Add HDL source files, constraints files, simulation files, block designs
IP Integrator
  Create, open, generate a block design
Run Simulation
  XSIM simulator included
  Behavioral, post-synthesis, post-implementation
RTL Analysis
  Open Elaborated Design button: Loads the elaborated RTL design

## Slide 15: Flow Navigator – RTL Project, cont’d…
Run Synthesis
  Timing driven
  Open Synthesized Design button: Loads synthesized netlist
Run Implement button: Runs implementation tools
  link, opt, power_opt, place, phys_opt, and route
  Open Implemented Design button: Loads implemented design
Program and Debug: Launches programming and debugging tools
  Open Hardware Manager to program the FPGA
  Hardware Manager also contains debug capabilities

## Slide 16: Simulation
The Vivado simulator, XSIM, supports RTL, netlist, and timing simulation
Part of the Vivado installation

## Slide 17: Adding Testbench Files
Testbench sources (*.V or *.VHD) must be added separately from design sources
  In the Flow Navigator, click Add Sources
  Select Add or Create Simulation Sources option and click Next
  Click on the Green + button, add files…, add directories… if the testbench file is already available or click on Create File… button to create a new testbench file
  Select a file type- Verilog, Verilog Header, SystemVerilog, or VHDL
  Browse to an existing testbench or enter a filename to create

## Slide 18: Simulation Settings
Allows selection of compilation and simulation properties
  From the Flow Navigator, click Simulation Settings
  The simulation top module is the testbench you have written and specify
  Additional options can be entered
    More Compilation Options field under Compilation tab
    More Simulation Options field under Simulation tab
Refer to the Vivado Design Suite Simulation Guide (UG900) for more information

## Slide 19: Simulation Results
Graphical waveform display
Toolbar buttons for adding markers, measuring delays, and zooming
Buses can be expanded to view individual signals
Dividers can be inserted to visually isolate groups of related signals
Console displays any messages output from testbench
By default, the top-level signals are displayed

## Slide 20: Outline
Vivado IDE Features and Benefits
Vivado Design Suite Introduction
Vivado Design Flow

## Slide 21: Xilinx Design Flow
Translate
Map
Place & Route
Plan & Budget
HDL RTL
Simulation
Synthesize
to create netlist
Functional
Simulation
Attain Timing
Closure
Timing
Simulation
Implement
Create Code/
Schematic
Generate BIT File
Configure FPGA

## Slide 22: Design Entry
Plan and budget：原理图
Create code: 生成.v文件
Create designs in HDL or Schematic

## Slide 23: RTL 分析
寄存器传输级（RTL，Register Transfer Level）：指不关注寄存器和组合逻辑的细节，通过描述寄存器到寄存器之间的逻辑功能描述电路的HDL层次。
Notes: 其他仿真。是指提取有关的器件延迟、连线延时等时序参数，并在此基础上进行的仿真，它是非常接近真实器件运行情况的仿真。

## Slide 24: Synthesis
After coding up your HDL code, you will need a tool to generate a netlist (NGC or EDIF)
  所谓综合(Synthesize) 是指将xxx.v文件输入翻译成由与、或、非门等基本逻辑单元组成的门级连接，并根据设计目标和要求优化所生成的逻辑连接，编译生成门级网表文件Netlist文件，表示自动生成的门级逻辑结构网表。
Generate a netlist file
Notes: 其他仿真。是指提取有关的器件延迟、连线延时等时序参数，并在此基础上进行的仿真，它是非常接近真实器件运行情况的仿真。

## Slide 25: What is a Netlist?
A Netlist is a description of your design
  Consists of cells, pins, port and nets
  Cells are design objects
    Instances of user modules/entities
    Instances of library Basic Elements (BELs)
      LUTs, FF, RAMs, DSP cells, etc…
    Generic technology representations of hardware functions
    Black boxes
  Pins are connection points on cells
  Ports are the top level ports of your design
  Nets make connections between pins and from pins to ports

## Slide 26: Netlist Objects
Notes: Ports are the primary inputs and outputs of the current design (normally the top level module).
Pins are the connections to instances – both instantiations of hierarchical objects and primitive cells.

## Slide 27: Functional Simulation
行为级仿真（behavioral simulation）：是指仅对逻辑功能进行测试模拟，以了解其实现的功能是否满足原设计的要求，行为仿真过程没有加入时序信息，不涉及具体器件的硬件特性，如延时特性。
其他仿真：是指提取有关的器件延迟、连线延时等时序参数，并在此基础上进行的仿真，它是非常接近真实器件运行情况的仿真。
Notes: 其他仿真。

## Slide 28: Implementation
Consists of three phases
  Translate: Merge multiple design files into a single netlist
  Map: Group logical symbols from the netlist (gates) into physical components (slices and IOBs)
  Place & Route: Place components onto the chip, connect the components, and extract timing data into reports
  注：实现主要根据不同的FPGA来具体的细化之前综合得到的网表。比如说工具可以具体的算出某个信号的延迟是多少。其中包括多少的走线延迟和多少的组合逻辑延迟。然后最后根据FPGA的内部结构决定把这个门放到哪里。
Translate
Map
Place & Route
Implement
. . .
.
.
.
Netlist Generated From Synthesis
.
.
.
Process a netlist file

## Slide 29: Configuration
Once a design is implemented, you must create a file that the FPGA can understand
  This file is called a bitstream: a BIT file (.bit extension)
The BIT file can be downloaded
  Directly into the FPGA
    Use a download cable such as Platform USB
  To external memory device such as a Xilinx Platform Flash PROM
    Must first be converted into a PROM file
Testing and Verification